## Slide 1: Creating and Using Python Virtual Environments (On HPCs and Other Systems)
LTC Smith
OA3802

## Slide 2: HPC Roadmap
Daily Lessons (with practical exercises):
  Day 1 Basics: Logging on, SSH and SFTP connections, getting oriented
  Day 2 Parallel Computation: Submitting and Running batch Jobs using Slurm
  Day 3: Using Python and Other Software with HPCs
    Day 3.5 Detour: Creating and Using Virtual Environments (on HPCs and other systems)
  Day 4+: HPC Extensions, Handling Big Data, Web Apps with HPC
HPC Lab: Implementing Combat Simulations on HPC, using material up through “Using Python” lesson.

## Slide 3: Virtual Environments
What is a Virtual Environment?
As we’ve seen so far in this course, user experience may vary when running the same code (bash, python, or anything else)
Virtual Environments help ensure user experience DOES NOT VARY by creating isolated and reproducible python environments
Why use a virtual environment?
Ensure consistent behavior of same code for different users
Ensure consistent behavior of same code on different systems
Allow different projects on same system to use different versions of python packages

## Slide 4: Virtual Environments on NPS HPC
Lets follow the NPS HPC guide for setting up virtual environments: Create a Python or Conda virtual environment - High Performance Computing - NPS Wiki
Two common methods for setting up virtual environment:
  Python: Use python’s venv package
  Conda: Use alternate package and environment management tool from Anaconda
We will explore “venv” method here, but both methods are widely used.

## Slide 5: Starting Python Script
In your “py” folder on HPC, create the “test_venv.py” file.
Try to run it:
  Launch interactive shell with salloc.
  Load default python module with module load lang/python
  Run script with python test_venv.py.
Did it work? Probably not!
May have gotten error such as ModuleNotFoundError: No module named 'faker’
For this code to work, we need our python environment to have numpy, pandas, and faker installed.
import sys
print("Hello from python! Using ",sys.version)
#Record current time for debugging
from datetime import datetime
now = datetime.now()
current_time = now.strftime("%D %H:%M:%S")
print("Current Time =", current_time)
#Try numpy and pandas as well
import numpy as np
import pandas as pd
print(f"{np.__version__ = }")
print(f"{pd.__version__ = }")
#Try to use faker as well
print('Some fake names using faker...\n')
from faker import Faker
fake = Faker()
for _ in range(5):
print(fake.name())
test_venv.py

## Slide 6: Create a Virtual Environment
OK, lets create a virtual environment on HPC using python’s venv package.
Launch interactive shell with salloc, and load desired python version. Recommend loading newest one, module load lang/python/3.11.2.
Create a new virtual environment named “comp3” with
python -m venv /smallwork/$USER/comp3
  NPS HPC recommends using /smallwork directory to better handle large number of files created by virtual environments
  The $USER variables stores current user’s username, so same code will work for any user running it
Activate new environment by running
source /smallwork/$USER/comp3/bin/activate
After activating, you should see the new (comp3) environment listed before your prompt.
  You may ALSO see the (base) environment. If so, you have a (base) conda environment and a (comp3) python venv environment. The first environment is the active one.
(base) [matthew.smith@compute-0-15 py]$ source /smallwork/$USER/comp3/bin/activate
(comp3) (base) [matthew.smith@compute-0-15 py]$

## Slide 7: Setting Up Virtual Environment
We can now set up the (comp3) environment by “pip installing” any packages into it.
First, run pip list to view all packages. If this is a new environment, you won’t see much.
You may have also gotten notice that a new release of pip is available. If so, go ahead and run the new command, something like pip install --upgrade pip
While the (comp3) environment is active, install the following, and then re-run pip list to confirm they were installed.
  pip install numpy
  pip install pandas
  pip install faker
Now, try to re-run python test_venv.py. Does it work?
Note: The slow process of downloading and installing new packages only needs to be done one time. After that, the packages are immediately available as soon as we activate the comp3 environment. To see this, can navigate to the /smallwork/$USER/comp3 folder, and you’ll see that all your installed packages show up in the “bin” folder.

## Slide 8: Using Virtual Environment in Batch Script
You can activate your new virtual environment within a batch script.
Create “test_venv.sh” in “py” folder, and run batch job with sbatch test_venv.sh, and it should work!
#!/bin/sh
#SBATCH --output=output/out_venv.txt
. /etc/profile
##module load lang/python #venv doesn’t
## need you to load this
source /smallwork/$USER/comp3/bin/activate
python test_venv.py
test_venv.sh
Note: When you activate the (comp3) environment, it automatically loads the python version (e.g. 3.11.2), so technically don’t need to run module load lang/python.

## Slide 9: Closing or Changing Virtual Environments
To stop using (comp3), simply run deactivate.
(comp3) (base) [matthew.smith@submit-1 py]$ deactivate
(base) [matthew.smith@submit-1 py]$
To overwrite (comp3), we have to add --clear to the venv creation command. Without --clear, venv will NOT overwrite an existing environment
python -m venv /smallwork/$USER/comp3 –clear
To delete a virtual environment, need to delete the venv directory and all its contents:
rm –r /smallwork/$USER/comp3

## Slide 10: Reproducing a Virtual Environment
We can install multiple packages at once by reading them in from a file, typically called “requirements.txt”.
pip install –r requirements.txt
We can create the requirements file for any environment by running pip freeze.
  Running pip list simply displays packages to screen
  Running pip freeze outputs packages in the format needed for a requirement.txt file
  Can create file with pip freeze > requirements.txt
Note: The requirement.txt file captures all packages, but not the python version number (e.g. 3.11.2). See the Pin Your Dependencies section of Real Python tutorial for more discussion.

## Slide 11: Python venv Recap
Task | Command
Create virtual environment | python -m venv /smallwork/$USER/comp3
Activate environment | source /smallwork/$USER/comp3/bin/activate
Install new packages into environment (run while environment is activated) | pip install package_name
Install all packages in a requirements file | pip install -r requirements.txt
List all installed packages | pip list
List all installed packages in requirements.txt format | pip freeze To create file: pip freeze > requirements.txt
Deactivate environment | deactivate
Overwrite environment | python -m venv /smallwork/$USER/comp3 --clear
Delete environment | rm –r /smallwork/$USER/comp3
Commands to set up virtual environment named “comp3” on NPS HPC.

## Slide 12: Conda Virtual Environments
Conda (from the Anaconda company) is an alternate approach to managing packages and virtual environments.
Conda gets packages from repo.anaconda.com (with conda install) instead of from Python Package Index (PyPI) (with pip install)
  Anaconda repo is similar but not identical to PyPI, and also allows for inclusion of non-python packages that might be relevant for data science.
Useful links:
  Using conda on NPS HPC: Create a Python or Conda virtual environment - High Performance Computing - NPS Wiki
  Quick discussion of conda vs venv: Python Virtual Environments: A Primer – Real Python
  Official conda docs (contains a useful cheet sheet): Managing environments — conda 24.9.2.dev13 documentation

## Slide 13: Conda on NPS HPC
Task | Command
Create virtual environment | conda create --prefix /smallwork/$USER/myconda1
Activate environment | conda activate /smallwork/$USER/myconda1
List all conda environments | conda env list or conda info --envs
Install new packages into environment (run while environment is activated) | conda install package_name
List all packages installed in current environment | conda list
Create env from file | conda env create -f environment.yml
Create env file | conda env export > environment.yml
Deactivate environment | conda deactivate
Delete environment | conda remove -n myconda1 --all
Commands to set up conda environment named “myconda1” on NPS HPC.
Need to first load miniconda, e.g with
module load lang/miniconda3/23.1.0

## Slide 14: Setting Default Environment
If you want to automatically activate a given virtual environment, you can add a line like this to your .bash_profile file:
source /smallwork/$USER/comp3/bin/activate
It will then take effect every time you log in (to have it take effect without logging out and logging back in, can run source ~/.bash_profile)
May also want to check your .bashrc file to see if there are any conda environments activated by default for all new shells
  Note that .bash_profile runs when you log onto hamming, and .bashrc runs whenever you start a new shell, including when you start an interactive shell with salloc.

## Slide 15: Resources
NPS HPC guide for setting up virtual environments: Create a Python or Conda virtual environment - High Performance Computing - NPS Wiki
Official Python docs on venv: venv — Creation of virtual environments — Python 3.13.0 documentation
Official conda User Guide: User guide — conda 24.9.2.dev12 documentation. For instructions on virtual environments, see “Getting Started” and “Working with Environments” pages. Great cheat sheet as well.
Excellent and thorough tutorial on python virtual environments: Python Virtual Environments: A Primer – Real Python. This is focused on python venv approach, but also touches on alternate approaches like conda and virtualenv (a popular tool with more functionality than venv).
Setting up python virtual environments on VSCode (includes both venv and conda): Using Python Environments in Visual Studio Code.